STATIC VOLTAGE STABILIZER

INTRODUCTION

Powercon’s Static Voltage Stabilizer is an IGBT based PWM type buck-boost voltage stabilizer which has tight regulation and fast correction speed which is impossible to obtain using conventional methods such as servo voltage stabilizers, SCR / triac type stabilizer, relay type stabilizer etc.

This is an SMPS type voltage stabilizer for mains voltage (AC input and AC output). This is a new switching topology where PWM is made directly in AC-to-AC switching, without any harmonic distortion. In this topology there is no need to convert the AC input to DC and again convert it back to regulated AC output. This simplifies the design, reduces the component count and improves the efficiency and reliability. The power stage is an IGBT chopper control. The chopping frequency is around 20KHz which ensures absolutely silent operation and pure sine wave output (no waveform distortion).

The control section is based on dsPIC controller which ensures quick correction of output which is not possible in conventional relay type stabilizer or servo controlled stabilizers. The circuit is having LCD for display which will show all parameters like: input voltage, output voltage, connected load, your company name (We will program your company name in the dsPIC at the time of technology transfer) etc.

Since the circuit is fully solid state (no mechanical or moving parts) there will not be any wear and tear like the brush tear in servo stabilizer or relay degrading in relay based stabilizer.

This is specially useful in places where we need very fast correction speed, constant output voltage, overload current limiting and short circuit protection, soft start, high voltage cut-off and low voltage cut-off, automatic bypass, no wear and tear, long life and maintenance free which is impossible with other conventional relay type or servo control stabilizers.

WORKING

In this IGBT based PWM type static voltage stabilizer only the difference voltage is switched through IGBT and will be added or subtracted from the mains. This is done electronically without any step changing in voltage which occurs when the system regulates. This is achieved by a feedback control system using digital signal processor (DSP). The output voltage is sensed by the DSP and corrections are made by varying the duty cycle of the PWM.

This stabilizer boosts up the voltage if it is low and bucks the voltage if it is high.

This means, we can use discrete IGBTs and make the circuit very compact and very high efficient. The efficiency in worst case will also be above 97%. This stabilizer is ideal for mobile towers, CNC machines, medical equipment, textile industries, power plants and any industrial product that needs tight regulation and fast correction. We can also use this for Air Conditioners, refrigerators, motor, pump etc.

FEATURES

- Direct AC-AC conversion without rectifying to DC improves the efficiency, reliability and reduces the components.

- Rapid cycle by cycle correction of output. It can correct sudden fluctuation in the line voltage. For example using a welding machine in the same line will cause sudden fluctuation in the line voltage which cannot be corrected with conventional relay type and servo controlled voltage stabilizers, where Static Voltage Stabilizer can correct it.

- Output regulation of +/- 1% which is impossible in conventional stabilizer.

- No distortion in output waveform.

- Overload cutoff and short circuit cut off

- Over voltage and under voltage cutoff.

- Automatic bypass incase of failure.

- LCD display for displaying all parameters and our company name.

- Compact size and light weight

- 20KHz PWM control

- IGBT power stage. Highly reliable.

- Fully solid state. No moving part, hence more life and no maintenance.

- Silent operation.

RELIABILITY

- Over load and short circuit protection

- High input voltage cut off

- Low voltage cut off

- Wear and tear

All the above protections and safety measures are not incorporated in the conventional stabilizers and that is what makes our differential power mode static stabilizer very reliable and unique.

Comparison chart between POWERCON’S Servo voltage stabilizer

& POWERCON’S Static voltage stabilizer

| Type of stabilizer |  |  |
| --- | --- | --- |
|  | Advantages | Disadvantages |
| Servo voltage | > Low technical skill | > Wear and tear due to the |
| stabilizer |  | mechanical movement, requires |
|  | > Less number of | periodic replacement of brushes |
|  | components |  |
|  |  | > Due to low correction speed |
|  | > Easy to manufacture | there will be voltage overshoot |
|  |  | and voltage dip |
|  | > High efficiency |  |
|  |  | > Heavy and bulky |
|  |  | > No inrush current limiting for |
|  |  | surge loads |
| Powercon’s IGBT | > No moving part, less | > Not cost effective in lower KVA |
| PWM static | maintenance | (below 2KVA) |
| voltage stabilizer |  |  |
|  | > Tight regulated output +/- |  |
|  | 1% |  |
|  | > Fast correction speed – |  |
|  | over 20000V per second |  |
|  | > Low cost |  |
|  | > High efficiency |  |
|  | > It has inrush current |  |
|  | limiting for surge loads |  |
|  | > Highly reliable |  |

SPECIFICATIONS SHEET FOR POWERCON’S STATIC VOLTAGE STABILIZER FOR THREE PHASE

Capacity in KVA       :        		6KVA to 100KVA (Three phase)

Technology	            :   		DSP based IGBT PWM switching

Normal operating

Input voltage              : 		Three phase (standard):-     340-480 volts ac 4-wire,50 Hz

(typical output regulation 		Three phase (customizable):-   360-470 volts ac 4-wire,50 Hz

within +/- 1% nominal)			Three phase (customizable):-   320-480 volts ac 4-wire,50 Hz

Three phase (customizable):-   295-500 volts ac 4-wire,50 Hz

Three phase (customizable):-   360-460 volts ac 4-wire,50 Hz

Nominal frequency     :		47-63 Hz

Nominal output          :		400 volts ac, Three phase

Voltage				410 volts ac, Three phase

415 volts ac, Three phase

Power Efficiency         :		over 97%

(typical with 20-100% load

conditions & worst incoming voltage)

Voltage regulation       :		+/- 1%

( typical, excluding meter error )

EMI filter		 :		Equipped with Emi filtering for proper operating of the unit

Annunciation                : 		LED display for Regulation mode & Fault conditions

Ambient temperature  :  		0 to + 45 centigrade (32 to+ 113 ferhehite ). 10 to 90% Rh non-condensing

Cooling method           :		Fan cooled

Overload & short

circuit Protection         :		Through suitably rated input circuit breaker

Automatic Bypass        :		Regulator engine will be automatically bypassed when

there is a fault condition

Warranty                      :		One year limited warranty, covering repair / replacement

of defective parts

Notes  :

- Nominal output voltage can be factory preset at any value between 215 to 240 P-N.

Regulation range will accordingly shift

- All models are optionally available with additional 400 Volts to 200 Volts step down transformers.

- Please ask if any non – standard range of customized feature is required.

SPECIFICATIONS SHEET FOR POWERCON’S STATIC VOLTAGE STABILIZER FOR SINGLE PHASE

Capacity in KVA       :        		2KVA to 25KVA (Single phase)

Technology	            :   		DSP based IGBT PWM switching

Normal operating

Input voltage              :       		Single phase (standard):-  170-290 volts ac 2-wire,50 Hz

(typical output regulation

within +/- 1% nominal)

Nominal frequency     :		47-63 Hz

Nominal output          :		230 volts ac, Single phase

Voltage

Power Efficiency         :		over 96%

(typical with 20-100% load

conditions & worst incoming voltage)

Voltage regulation       :		+/- 1%

( typical, excluding meter error )

EMI filter		 :		Equipped with Emi filtering for proper operating of the unit

Annunciation                : 		LED display for Regulation mode & Fault conditions

Ambient temperature  :  		0 to + 45 centigrade (32 to+ 113 ferhehite ). 10 to 90% Rh non-condensing

Cooling method           :		Natural cooled

Overload & short

circuit Protection         :		Through suitably rated input circuit breaker

Automatic Bypass        :		Regulator engine will be automatically bypassed when

there is a fault condition

Warranty                      :		One year limited warranty, covering repair / replacement

of defective parts

Notes  :

- Nominal output voltage can be factory preset at any value between 215 to 240 P-N.

Regulation range will accordingly shift

- All models are optionally available with additional 400 Volts to 200 Volts step down transformers.

- Please ask if any non – standard range of customized feature is required.

Ratings

| Supply System | Input Voltage* |  | Ratings (KVA) |
| --- | --- | --- | --- |
| Single phase | 170-290V | Air cooled | 3, 5, 10, 7.5, 10, 15, 20, 25 KVA |
| Three phase | 340-480V | Air cooled | 10, 15, 20, 25, 30, 40, 50, 60, 75, 100 KVA |

APPLICATIONS

- CNC & Robotics

- Auto & Auto ancillary

- Oil & Gas

- Textile Spinning, Processing,  knitting & weaving

- Engineering & Process Industry

- Wood Cutting

- Radar & Telecommunication

- R&D, Testing Diagnostics

- Plastic Processing

- Printing & Packaging

- Security & Surveillance

- Building Management